FINAL CERTIFICATE OF OCCUPANCY REQUIREMENTS

CHECK OFF LIST

(         Driveway Apron Paved

(	House number attached				(   Garage

(   1) Firewall 5/8” Firecode sheetrock & Tape

(	Outside Steps & Porch				(   2) Fire Doors self closing – 1 Hour Rated

( 1) 3 Steps need railings 36” (One side)		(   3) Door opener safety stops

( 2) Above 30” need balusters every 4”		(   4) Floor Pitched back to garage doors

(	Outside Receptacle GFI (Must be WR type)

(	Dishwasher Vacuum Break and Air Hammers

(	Kitchen sink operational

(	Outlets covered GFCI & AFCI

(	Kitchen outlets AFCI & GFCI

(	Outlet in island (No more than a 6” overhang)

(	Appliance wires in Boxes if not attached

(	One bathroom operational with GFCI outlets

(	Patio doors blocked or opening on finished patio

(	Egress doors & windows proper size

(	Joist hangers or ledger steps

- (Smoke detectors all floors) one in each sleeping area and in hallway adjacent to bedrooms

- Smoke detectors within 20’ of a bath with a shower or kitchen shall be photo electric

- Carbon Monoxide in areas adjacent to bedrooms

(	Stairway rails & Balusters main & basement

(	Lally column plates nailed

(	Chimney

(  1) Fire stops/ Aluminum not acceptable – 26 gauge

(  2) Clean Outs 16” above basement floor

(  3) Clearance from combustible materials 18” min. (cleanout) 2” around masonry

- 4) Power vent clearance 4’ from any window or door

- 5) Disclosure form signed & completed by the mason

(	Breaker Box						Oil Tank

(  1) Cold water ground				(  1) Vent installed

- 2) Breakers labeled				(  2) 12” legs only

- 3) Arc Fault breakers where required by code	(  3) Oil line protected and secured

- 4) Energy Efficiency Certificate			(  4) Filter

# Text boxes

# Town of Gorham

Code Enforcement Department

## Municipal Center Room 143

75 South Street, Suite 1

Gorham, Maine 04038

(207) 222-1605

(207) 839-4793 Fax

www.gorham-me.org